## Slide 2
Specify domain’s starting fluid composition on the Initial pane
Clean water

## Slide 3
Inlet fluid “contaminated” enters the domain from t = 0 to 2 years
Inlet fluid “flush” enters the domain from t = 2 to 10 years
Define the reaction intervals. Specify what fluids flow into the domain, and when.
Click to add a new reaction interval

## Slide 4
Inlet fluid named “contaminated” carries Pb++ pulse into the domain
The various inlet fluids are defined on the Fluids pane
Clean rinse water: negligible Pb++ in the “flush” inlet fluid
Click to add a new fluid

## Slide 5
Specify domain size and gridding on the Domain pane.
Domain is 1 km long, divided into 400 nodal blocks

## Slide 6
Specify flow rate on the Flow pane.
Set specific discharge or hydraulic head/ potential drop
Set flowrate for 1st and 2nd reaction intervals individually, or set one flowrate for all intervals

## Slide 7
Used to calculate coefficient of hydrodynamic dispersion.
Porosity affects groundwater velocity.
Run → Go
traces the model
Set various mass transport properties on the Medium pane.

## Slide 8
Pb++ pulse transported through the domain by advection, dispersion, and diffusion.