## Slide 2
File → Open →
Thermo Data…
thermo_hmw.tdat is the Harvie-Moller-Weare formalism of the Pitzer equations.
When dealing with concentrated fluids, it’s a good idea to use a thermo dataset utilizing the Pitzer equations.

## Slide 3
Set the composition of the initial fluid on the Basis pane.
1 kg solvent water plus solutes define seawater
Initial fluid is equilibrated with CO2 in the atmosphere

## Slide 4
Set up a titration path on the Reactants pane.
add → Simple → Aqueous… H2O
Simulate evaporation by removing solvent water from the system (react a negative mass)

## Slide 5
Minerals precipitate and dissolve during the evaporation of seawater.

## Slide 6
Config →
Stepping…
Flow-through option doesn’t allow precipitated minerals to dissolve back into the fluid
Repeat assuming fractionation of the precipitated minerals

## Slide 7
Minerals that precipitate are not allowed to dissolve back into the evaporating seawater.