## Slide 2
Config →
Dual Porosity…
On/off toggle
40% of the aquifer is stagnant.
Characteristic dimension of the stagnant zone
In a dual porosity model, each nodal block is divided into a free-flowing zone and a stagnant zone.
Diffusion coefficient, thermal conductivity, porosity of stagnant zone default to free-flowing values unless you set them here.

## Slide 3
Specify domain’s starting fluid composition on the Initial pane
Clean water

## Slide 4
Inlet fluid “contaminated” enters the domain from t = 0 to 2 years
Inlet fluid “flush” enters the domain from t = 2 to 10 years
Define the reaction intervals. Specify what fluids flow into the domain, and when.
Click to add a new reaction interval

## Slide 5
Inlet fluid named “contaminated” carries Pb++ pulse into the domain
The various inlet fluids are defined on the Fluids pane
Clean rinse water: negligible Pb++ in the “flush” inlet fluid
Click to add a new fluid

## Slide 6
Specify domain size and gridding on the Domain pane.
Domain is 1 km long, divided into 100 nodal blocks

## Slide 7
Specify flow rate on the Flow pane.
Set specific discharge or hydraulic head/ potential drop
Set flowrate for 1st and 2nd reaction intervals individually, or set one flowrate for all intervals

## Slide 8
Set various mass transport properties on the Medium pane.
Used to calculate coefficient of hydrodynamic dispersion.
Porosity of the free-flowing zone.
Run → Go
traces the model

## Slide 9
Pb++ travels from one nodal block to another only through the free-flowing volume, but it can diffuse into and out of the stagnant zones.