## Slide 2
Porewater temperature is 40°C
Specify domain’s starting fluid temperature on the Initial pane

## Slide 3
A single inlet fluid flows into the domain for 20 days.
Define the reaction intervals. Specify what fluids flow into the domain, and when.

## Slide 4
A 200°C injectate will displace the initial fluid
The inlet fluid is defined on the Fluids pane

## Slide 5
Specify domain size and gridding on the Domain pane.
Domain is 2000 cm long, divided into 40 nodal blocks
Radial domain set in this example

## Slide 6
Specify flowrate on the Flow pane.
Injection pressure 0.7 atm greater than formation pressure

## Slide 7
Set various thermal properties on the Medium pane.
Can include transient heat sources or sinks within the domain.
Set thermal conductivity of porous medium to model heat conduction.
Run → Go
traces the model
Set heat capacity of the fluid and rock to simulate heat transfer by advecting groundwater.

## Slide 8
Hot water is injected into the domain’s inlet. Heat transported by advection and conduction.