## Slide 1
Right-click on unit field to convert units
GSS is a spreadsheet for manipulating and plotting geochemical data.

## Slide 2
Enter chemical data for one or more samples in GSS, then perform geochemical calculations.
+ analyte → Calculate…

## Slide 3
For variable type, choose Mineral saturation
Select a mineral then click Apply
Calculated saturation indices added to spreadsheet

## Slide 4
For variable type, choose Fugacities
Select a gas then click Apply
Calculated gas fugacity added to spreadsheet

## Slide 5
For variable type, choose Chemical parameters
Select analytes then click Apply
Calculated analytes appear below your original data

## Slide 6
For variable type, choose Chemical parameters
Select one or more parameters, then click Apply
Nernstian Eh is calculated where analyses of elements are provided in multiple oxidation states.

## Slide 7
For variable type, choose Species concentrations
Select a species, then click Apply
The concentrations of the actual species in solution are reported.
You can also calculate species activities or activity coefficients

## Slide 8
GSS can compare replicate analyses to verify the results agree to within an error tolerance.
Analysis →
Compare Replicates…
Replicate analyses or splits of a single sample

## Slide 9
Set an error tolerance
Check marks indicate an acceptable coefficient of variance between replicates.
X’s appear where the error tolerance is exceeded.
Select samples to compare then click Apply

## Slide 10
Graphs → Time Series Plot
You can display your data in Time Series and XY plots

## Slide 11
You can choose from a variety of water chemistry plots
Change color, marker, and size for sample 02-2397.
Graphs → Piper Diagram