## Slide 2
Negligible ferric iron (HFO) in initial system
Considerable Pb++ in initial system
Specify domain’s starting fluid composition on the Initial pane

## Slide 3
Define the reaction intervals. Specify what fluids flow into the domain, and when.
A single inlet fluid flows into the domain for 10 years.
Click to add a new reaction interval

## Slide 4
Inlet fluid carries ferric hydroxide colloid into the domain
Negligible Pb++ in inlet fluid
The inlet fluid is defined on the Fluids pane

## Slide 5
Specify domain size and gridding on the Domain pane.
Domain is 1 km long, divided into 100 nodal blocks

## Slide 6
Specify flow rate on the Flow pane.
Set specific discharge or hydraulic head/ potential drop

## Slide 7
Set various mass transport properties on the Medium pane.
Colloid migrates by advection and dispersion

## Slide 8
Kd describes distribution coefficient between Pb++ and immobile aquifer sediments
Surface complexation dataset for hydrous ferric oxide.
File → Open → Sorbing Surfaces…
You can add any number of sorbing surfaces.
Set mobility in the domain to 1 to make HFO and its sorbate a mobile colloid.

## Slide 9
If you check to include “sorbate”, the total Pb++ concentration defined for each fluid (Initial and Fluids panes) is distributed between solution and surfaces.
Config → Iteration
Run → Go
traces the model

## Slide 10
Initially Pb++ almost entirely sorbed to immobile aquifer sediments (>Pb++).
Fluid transports ferric hydroxide colloid through aquifer.
Pb++ scavenged from aquifer sediments (>Pb++) onto mobile colloid surface (>(s)FeOPb+).