## Slide 2
Clean water
Specify domain’s starting fluid composition on the Initial pane

## Slide 3
Inlet fluid “contaminated” enters the domain from t = 0 to 2 years
Inlet fluid “flush” enters the domain from t = 2 to 10 years
Define the reaction intervals. Specify what fluids flow into the domain, and when.
Click to add a new reaction interval

## Slide 4
Inlet fluid named “contaminated” carries Pb++ and Br− into domain
Clean rinse water: negligible Pb++ and Br− in the “flush” inlet fluid
Click to add a new fluid
The Br− acts as a tracer in our model.
The various inlet fluids are defined on the Fluids pane

## Slide 5
Specify domain size and gridding on the Domain pane.
Domain is 1 km long, divided into 400 nodal blocks

## Slide 6
Specify flow rate on the Flow pane.
Set specific discharge or hydraulic head/ potential drop
Set flowrate for 1st and 2nd reaction intervals individually, or set one flowrate for all intervals

## Slide 7
Set various mass transport properties on the Medium pane.
Used to calculate coefficient of hydrodynamic dispersion.
Porosity affects groundwater velocity.

## Slide 8
Kd describes distribution coefficient between Pb++ and aquifer sediments. Br− does not sorb.
Run → Go
traces the model
File → Open → Sorbing Surfaces…
You can add any number of Kd, Freundlich, or Langmuir isotherms.
You can also account for ion exchange or surface complexation using the two-layer model.

## Slide 9
Sorption retards Pb++ transport relative to nonreactive tracer Br−.