## Slide 2
Specify flow rate on the Flow pane.
GWB will use Darcy’s law to calculate discharge from the viscosity, permeability, and driving force.
You can set discharge directly...
... or set the driving force for flow (the drop in head or hydraulic potential across the domain).

## Slide 3
kx is permeability along x in darcys
Φ is porosity
A, B, and Am are empirical constants
Xm are the volume fractions of an
arbitrary set of minerals indexed by m
The GWB programs use a correlation to calculate permeability:

## Slide 4
You can set a value for the permeability directly
log kx = (A x Φ) + B
= (0 x 0.2) − 5 = −5
kx = 1e-5 darcys
A set to 0

## Slide 5
You can set permeability as a function of porosity
log kx = (A x Φ) + B
= (10 x 0.2) − 5 = −3
kx = 1e-3 darcys
You can set the initial value forΦ (porosity) at each node.

## Slide 6
You set the quantity of minerals on the Initial or Reactants pane.
Kaolinite initially occupies 5% of the porous media
(X1 = 0.05).

## Slide 7
You can set permeability as a function of porosity and the volume of one or more minerals.
log kx = (A x Φ) + B + (A1 x X1)
= (10 x 0.2) − 5 + (−40 x 0.05) = −5
kx = 1e-5 darcys
add → Kaolinite
Kaolinite decreases the permeability of the porous media.

## Slide 8
In X2t, you can set the anisotropy of the medium.
The medium is 10 times more permeable along the x-direction than along y.