## Slide 2
Clean water
Specify starting fluid composition on the Initial pane.

## Slide 3
Inlet fluid “contaminated” enters the domain from t = 0 to 2 years
Inlet fluid “flush” enters the domain from t = 2 to 10 years
Define the reaction intervals. Specify what fluids flow into the domain, and when.
Click to add a new reaction interval
You can add any number of reaction intervals.

## Slide 4
Inlet fluid named “contaminated” carries Pb++ pulse into the domain
You can define any number of unique fluid chemistries on the Fluids pane
Clean rinse water: negligible Pb++ in the “flush” inlet fluid
Click to add a new fluid

## Slide 5
Set flowrate for each reaction interval individually...
Set the flow field for each reaction interval on the Flow pane.
... or set one flowrate for all intervals
Run → Go
traces the model

## Slide 6
New: For irregular contaminant sources, use any number of boundary fluids and reaction intervals.
Pb++ contaminated water enters domain for two years then is flushed with clean water.

## Slide 7
Wells in X2t can have a different pumping rate and fluid chemistry for each well interval.
No pumping
Negative rate indicates extraction
Positive rate indicates injection
XY position of well
Choose from defined fluids